## Slide 1
Where AI can help
Realistic Datasets for Photons and Neutrons AI methodologies
McStas — neutrons
McXtrace — X-rays
Emmanuel FARHI · Synchrotron SOLEIL
PaNRAID School · supported by PEPR DIADEM

## Slide 2
TARGET
This school’s objective
2
Explore how AI can leverage simulated photon and neutron datasets to :
solve inverse problems (measurement → parameters)
optimize experiments (find best parameters)
train surrogate models (parameters → measurement)
For all this, we encourage you to use AI chats.

## Slide 3
X/n
Why "Photons and Neutrons"?
2
Shared X/n Physics and Simulation Capabilities
Similar Interaction Processes:
Absorption: Energy transfer to the material (e.g., photoelectric effect for X-rays, neutron capture).
Scattering:
Elastic: Structure analysis (e.g., Bragg diffraction for X-rays, neutron diffraction).
Inelastic: Dynamics analysis (e.g., Raman scattering for X-rays, neutron inelastic scattering).
Decay: Time-resolved studies (e.g., fluorescence, neutron activation).

## Slide 4
X/n
Why "Photons and Neutrons"?
2
Simulation Tools:
McStas: Monte Carlo simulator for neutron scattering instruments.
McXtrace: Monte Carlo simulator for X-ray instruments.
Both enable realistic modeling of beamlines, detectors, and sample interactions.
Why Simulations Matter:
Realism: Capture complex instrument geometries and material responses.
Flexibility: Test hypothetical setups.
Cost-Effective: Avoid expensive trial-and-error on real instruments/BL.

## Slide 5
Realistic datasets
Why Realistic AI Datasets?
2
The Problem with Experimental Data
Lack of Annotations:
  Raw data often lacks metadata (e.g., sample composition, instrument settings).
  Manual annotation is time-consuming and error-prone.
Publications as Implicit Annotations:
  Papers describe experimental conditions, but formats vary widely.
  Not machine-readable or standardized for AI training.

## Slide 6
Realistic datasets
Why Realistic AI Datasets?
2
The Power of Simulated Data
Controlled Parameters:
  Every input (e.g., sample thickness, detector angle) is known and adjustable.
  Outputs (e.g., scattering patterns, spectra) are directly linked to inputs.
Pipeline Workflow:
  Parameters → [Simulation (McStas/McXtrace)] → Virtual “Measurement”
Example: Simulate an experiment with varying incident energy.

## Slide 7
Realistic datasets
Why Realistic AI Datasets?
2
Inverse Problem:
Goal: Reconstruct input parameters from measured data.
AI Approach:
Measurement → [AI Algorithm] → Parameters
Example: Predict sample composition from a scattering pattern.

## Slide 8
Realistic datasets
Why Realistic AI Datasets?
2
Surrogate Models:
Purpose: Replace slow simulations with fast AI models.
Pipeline:
Parameters → [AI Model] → Virtual "Measurement" (faster)
Use Case: Real-time optimization of beamline configurations.

## Slide 9
Realistic datasets
Why Realistic AI Datasets?
2
Model optimization:
Purpose: Find best parameters to get min/max signal.
Pipeline:
Parameters → [AI Model] → Virtual "Measurement" (faster)
Use Case: Real-time optimization of beamline configurations.

## Slide 11
Thank you
Questions?
mcstas.org
mcxtrace.org
Peter Willendrup · pkwi@fysik.dtu.dk · DTU Physics
{presentation title
17
SUPPORTED BY