## Slide 1
A COMMON INTRODUCTION
McStas & McXtrace
Monte Carlo ray-tracing for neutron and X-ray instrumentation
McStas — neutrons
McXtrace — X-rays
Peter Willendrup · DTU Physics
PaNRAID School · supported by PEPR DIADEM

## Slide 2
PANRAID SCHOOL
Who's behind this school
McStas & McXtrace · Common Introduction
2
PaNRAID is organised with support from the France 2030 PEPR DIADEM programme, training researchers to combine McStas and McXtrace ray-tracing simulations with AI methods.
PARTNERS & SUPPORTING ORGANISATIONS

## Slide 3
AGENDA
What we'll cover
1
Shared origins & philosophy
One codebase family, two physics engines
2
The Monte Carlo ray-tracing idea
Why rays, weights, and randomness
3
Anatomy of a simulation
Instruments, components, and the ray state
4
Under the hood
DSL, code generation, and coordinate placement
5
Neutrons vs. X-rays
Where the two probes really differ
6
Community, use & getting started
License, ecosystem, and next steps
McStas & McXtrace · Common Introduction
3

## Slide 4
SHARED ORIGINS
One family, two probes
McXtrace was built on proven McStas technology — same architecture, adapted for X-rays.
1998
McStas is born
K. Nielsen & K. Lefmann, Risø.
Originally for triple-axis
spectrometer simulation.
2000s
Grows into a general tool
Adopted by DTU Physics, ILL,
PSI, University of Copenhagen,
ESS DMSC. GPL open source.
2009
McXtrace forks off
“Powered by McStas
technology.” Re-targeted at
X-ray optics & beamlines.
Today
Parallel development
Shared kernel philosophy,
separate physics & component
libraries, active communities.
Commonality: same domain-specific language, same component-based architecture, same open, community-driven development model.
McStas & McXtrace · Common Introduction
4

## Slide 5
THE CORE IDEA
Monte Carlo ray-tracing, in a nutshell
A statistical method born at Los Alamos in the 1940s (von Neumann, Ulam, Metropolis) for solving particle-transport problems by numerical experiment.
Both codes trace many independent rays (neutrons or photons) one at a time through the instrument.
Propagation in free space is deterministic — straight lines (plus gravity, for slow neutrons).
McStas & McXtrace · Common Introduction
5
Where physics is probabilistic — scattering, absorption, reflection — outcomes are Monte Carlo sampled.
Each ray carries a statistical weight rather than representing one real particle, so rare but important events can be sampled efficiently.
A single ray, one weight at a time
Weight p is adjusted multiplicatively at every interaction — the physical result is recovered statistically over many rays.

## Slide 6
SHARED ARCHITECTURE
Anatomy of a simulation
An instrument is an ordered chain of components in a shared lab coordinate system. Rays flow through it, changing state at each stop.
Source
injects rays
Optics
shapes the beam
Sample
the physics of interest
Monitor
records the result
Instrument: defines the lab coordinate system. Components: devices/features available in the instrument, each with its own function. Rays: passed from one component to the next, changing state along the way.
This chain — and the DSL that describes it — is identical in McStas and McXtrace.
McStas & McXtrace · Common Introduction
6

## Slide 7
COMMONALITY & DIFFERENCE
What travels through the beamline: the ray
Neutron ray · McStas
r
position (x, y, z)
v
velocity vector
t
time
s
spin / polarisation
p
statistical weight
Photon ray · McXtrace
r
position (x, y, z)
k
wave vector
φ, E
phase & polarisation (E-field)
t
time
p
statistical weight
Same idea, different carrier: both rays are position + time + statistical weight. The neutron adds mass, velocity and spin; the photon adds a wave vector, phase and field polarisation.
McStas & McXtrace · Common Introduction
7

## Slide 8
SHARED TAXONOMY, DIFFERENT PHYSICS
Component classes
Every instrument, in either code, is built from the same four component classes.
Class | McStas (neutrons) | McXtrace (X-rays)
Sources | Reactor / spallation moderator | Undulator, wiggler, bending magnet
Optics | Guides, mirrors, choppers, collimators | Mirrors, monochromator crystals, multilayers, slits
Samples | Powders, crystals, liquids, magnetism | Powders, crystals, multilayers, absorbing phantoms
Monitors | PSD / histograms / event lists | PSD / histograms / event lists (same concept)
Common to all components: they set, manipulate, or measure the state of the ray — and each is written as a self-contained, reusable code module.
McStas & McXtrace · Common Introduction
8

## Slide 9
UNDER THE HOOD
From instrument file to running simulation
.instr file
DSL describing the
instrument (readable text)
Parser
Lex & Yacc
compiler technology
Generated C
Portable ISO-C code,
only what you use
Executable
Compiled for your
platform & hardware
Same toolchain in both codes — the DSL grammar and code generator are shared.
Three levels of code, three audiences
Instrument file
MOST USERS
Existing examples, GUI-assisted, or written from scratch in the DSL.
Component file
ADVANCED USERS
Short, self-contained C code — easy to modify from an existing component.
Kernel
CORE DEV TEAM
Propagation, intersections, and the runtime library shared by all components.
McStas & McXtrace · Common Introduction
9

## Slide 10
SHARED SYNTAX
Placing components in space
Every component is placed with the same two statements, in both codes:
AT (x, y, z) RELATIVE <ref> ROTATED (rx, ry, rz) RELATIVE <ref>
<ref> can be ABSOLUTE (the lab frame), another component's name, or PREVIOUS.
z runs along the beam, y is vertical, x completes a right-handed frame.
Component authors choose whatever local origin is physically natural — the kernel handles the coordinate transforms between them.
AT and ROTATED can be fully decoupled, referring to different RELATIVE <ref>
Right-handed lab frame
McStas & McXtrace · Common Introduction
10
x
y
z
Particle beam
Vertical

## Slide 11
WHERE THEY DIVERGE
Neutrons vs. X-rays: key differences at a glance
 | Neutrons · McStas | X-rays · McXtrace
Probe | Neutral particle — mass, spin | Massless electromagnetic wave
Typical facility | Reactor or spallation source | Synchrotron or free-electron laser
Energy scale | meV (thermal / cold) | keV (hard X-ray)
Dominant interaction | Nuclear & magnetic scattering; deep penetration | Electronic scattering; surface-sensitive, strongly absorbed
What stays the same: the ray-tracing method, the DSL, the component architecture, and the statistical-weight formalism are identical — only the physics inside the components differs.
McStas & McXtrace · Common Introduction
11

## Slide 12
COMMUNITY & PRACTICALITIES
Open, portable, community-built
GPL
Open-source license
for both packages
3
Platforms: Linux,
macOS, Windows
175+
Components in the
shared-style libraries
30–40%
Of new components
come from users
Runs everywhere from a laptop to HPC clusters and GPUs (OpenACC) — the same generated C code, recompiled per target.
New components automatically fit the framework once written in structured, standard C.
Contributions require at least one test instrument and a documented header — then they join the shared contrib/ library.
Permanent staff at DTU Physics maintain the core; a wider network of institutes and students keeps both libraries growing.
McStas & McXtrace · Common Introduction
12

## Slide 13
ONE CORE TEAM, TWO NETWORKS
Who builds & maintains them
A shared core team at DTU Physics, plus partner institutes around each package.
McStas partner network
DTU Physics (core development)
European Spallation Source (ESS DMSC)
University of Copenhagen
Institut Laue-Langevin (ILL), Grenoble
Paul Scherrer Institute (PSI)
McXtrace partner network
Synchrotron SOLEIL
DTU Physics (core development)
University of Copenhagen
Further both codes benefit from the greater network of users across a plethora of use-cases and applications.
Several developers work across both projects — shared infrastructure means fixes and features often benefit both codes at once.
McStas & McXtrace · Common Introduction
13

## Slide 14
APPLICATIONS
What are they used for?
1
Instrument design
Planning and optimising new beamlines before they're built
2
Construction support
Verifying components and layouts during commissioning
3
Virtual experiments
Letting prospective users try an experiment before travelling to a facility
4
Data analysis
Comparing measured data against simulated instrument response
5
Teaching
Training students and new users in instrumentation & scattering methods
Both communities use their code across the full lifecycle — from first sketch to published data.
McStas & McXtrace · Common Introduction
14

## Slide 15
ECOSYSTEM
A shared, interoperable ecosystem
1
MCPL
The Monte Carlo Particle List format lets McStas, McXtrace and other transport codes (MCNP, Geant4, PHITS, …) exchange rays and couple simulations together.
2
Graphical interface
A common Python-based GUI supports building, running and browsing results for instruments in either code.
3
Plotting tools
A shared plotting toolchain (HTML/D3, pyqtgraph, matplotlib backends) visualises monitor output from both packages.
4
Packaging
Conda-forge distributions and cross-platform installers keep both codes easy to install on Linux, macOS and Windows.
McStas & McXtrace · Common Introduction
15

## Slide 16
GETTING STARTED
Where to go next
McStas
WEBSITE
mcstas.org
MAILING LIST
mcstas-users@mcstas.org
INSTALL
conda-forge · cross-platform installers
SOURCE
GitHub — McStasMcXtrace/McCode
McXtrace
WEBSITE
mcxtrace.org
MAILING LIST
mcxtrace-users@mcxtrace.org
INSTALL
conda-forge · cross-platform installers
SOURCE
GitHub — McStasMcXtrace/McCode
McStas & McXtrace · Common Introduction
16

## Slide 17
Thank you
Questions?
mcstas.org
mcxtrace.org
Peter Willendrup · pkwi@fysik.dtu.dk · DTU Physics
McStas & McXtrace · Common Introduction
17
SUPPORTED BY