## Slide 1
Seeking for AI
Realistic Datasets for Photons and Neutrons AI methodologies
McStas — neutrons
McXtrace — X-rays
Emmanuel FARHI · Synchrotron SOLEIL – Sept 2026
PaNRAID School · supported by PEPR DIADEM

## Slide 2
TARGET
This school’s objective
2
Explore how AI can leverage simulated photon and neutron datasets to:
Solve inverse problems (measurement → parameters)
Optimize experiments (find best parameters)
Train surrogate models (parameters → measurement)
For all this, we encourage you to use AI chats/agents.

## Slide 3
X/n
Why "Photons and Neutrons"?
2
Shared X/n Physics and Simulation Capabilities
Similar Interaction Processes:
Absorption: Energy transfer to the material (e.g., photoelectric effect for X-rays, neutron capture).
Scattering:
Elastic: Structure analysis (e.g., Bragg diffraction for X-rays, neutron diffraction).
Inelastic: Dynamics analysis (e.g., Raman scattering for X-rays, neutron inelastic scattering).
Decay: Time-resolved studies (e.g., fluorescence, neutron activation).

## Slide 4
X/n
Why "Photons and Neutrons"?
2
The Real World:
  Parameters → [Instrument] → “Measurement”
Simulation Tools:
McStas: Monte Carlo simulator for neutron scattering instruments.
McXtrace: Monte Carlo simulator for X-ray instruments.
Both enable realistic modeling of beamlines, detectors, and sample interactions.
Why Simulations Matter:
Realism: Capture complex instrument geometries and material responses.
Flexibility: Test hypothetical setups.
Cost-Effective: Avoid expensive trial-and-error on real instruments/BL.

## Slide 5
Realistic datasets
Why Realistic AI Datasets?
2
The Problem with Experimental Data
Lack of Annotations:
  Raw data often lacks metadata (e.g., sample composition, instrument settings).
  Manual annotation is time-consuming and error-prone.
Publications as Implicit Annotations:
  Publications describe experimental conditions, but formats vary widely.
  Not machine-readable or standardized for AI training.

## Slide 6
Realistic datasets
Why Realistic AI Datasets?
2
The Power of Simulated Data
Controlled Parameters:
  Every input (e.g., sample thickness, detector angle) is known and adjustable.
  Outputs (e.g., scattering patterns, spectra) are directly linked to inputs.
Pipeline Workflow:
  Parameters → [Simulation] → Virtual “Measurement”
Example: Simulate an experiment with varying incident energy.

## Slide 7
Realistic datasets
Why Realistic AI Datasets?
2
Inverse Problem:
Goal: Reconstruct input parameters from measured data.
AI Approach:
Measurement → [AI Algorithm] → Parameters
Example: Predict sample composition from a scattering pattern.

## Slide 8
Realistic datasets
Why Realistic AI Datasets?
2
Surrogate Models:
Purpose: Replace slow simulations with fast AI models.
Pipeline:
Parameters → [AI Model] → Virtual "Measurement" (faster)
Use Case: Fast phase-space exploration.

## Slide 9
Realistic datasets
Why Realistic AI Datasets?
2
Model optimization:
Purpose: Find best parameters to get min/max signal.
Pipeline:
Parameters → [Optimizer] → Best Parameters
Use Case: Optimization of beamline configurations.

## Slide 10
General AI Methodology
General AI Methodology
2
AI as a Universal Function Approximator:
Black Box Concept:
Input → [AI Model] → Output
Universal Approximation Theorem: A neural network can approximate any continuous function given sufficient data and complexity.
General Behavior:
All AI methods (CNNs, RNNs, SVMs) follow the same principle: map inputs to outputs via learned weights.
Differences lie in architecture, training efficiency, and interpretability.

## Slide 11
General AI Methodology
General AI Methodology
2
Training: The Core Process
Objective: Minimize the loss function (e.g., Mean Squared Error, Cross-Entropy).
Loss Function: Measures the difference between predicted and actual outputs.
Steps:
Forward Pass: Compute predictions for a batch of training data.
Loss Calculation: Evaluate how far predictions are from true values.
Backpropagation: Compute gradients of the loss with respect to weights.
Optimization: Update weights using an optimizer (e.g., Adam, SGD).

## Slide 12
General AI Methodology
General AI Methodology
2
Training: The Core Process
Key Factors for Success:
Data Quality: High-fidelity simulations with diverse parameters.
Model Architecture: Match complexity to the problem (e.g., CNNs for images, Transformers for sequences).
Hyperparameters: Learning rate, batch size, number of epochs.

## Slide 13
Lessons and praticals
What You Will Learn and Practice
2
Hands-on skills
Setting Up Simulations:
Configure beamlines/instruments in McStas (neutrons) and McXtrace (X-rays).
Define sample properties (e.g., crystal structure, composition).
Characterizing Models:
Check geometry (e.g., detector positions, slit sizes).
Extract parameters (e.g., resolution, flux) and results (e.g., spectra, diffraction patterns).

## Slide 14
Lessons and praticals
What You Will Learn and Practice
2
Hands-on skills
Generating Datasets:
Automate simulations across parameter ranges (e.g., vary samples).
Output: Labeled datasets of [parameters, virtual_measurements].
Apply AI :
Surrogate Modeling: generate virtual_measurements faster.
Solving Inverse Problems: get parameters from measurements.
Optimization: search fpr best parameters.

## Slide 15
Resources
What You Will Use
2
Your Laptop
High Performance Computing (MesoNET)
Remote Computing Service (DARTS@SOLEIL)
Your Brain

## Slide 16
Thank you
Questions?
mcstas.org
mcxtrace.org
Peter Willendrup · pkwi@fysik.dtu.dk · DTU Physics
{presentation title
17
SUPPORTED BY